# Generated by PNCconf at Thu May 16 21:32:27 2019
# If you make changes to this file, they will be
# overwritten when you run PNCconf again

[EMC]
MACHINE = EMCOTURN220
DEBUG = 0

[DISPLAY]
DISPLAY = gmoccapy
EMBED_TAB_NAME = GladeVCP
EMBED_TAB_COMMAND = halcmd loadusr -Wn gladevcp gladevcp -c gladevcp -H gvcp_call_list.hal -x {XID} gvcp-panel.ui

EMBED_TAB_NAME = ATC
EMBED_TAB-LOCATION = BOX_CUSTOM_4

POSITION_OFFSET = RELATIVE
POSITION_FEEDBACK = ACTUAL
MAX_FEED_OVERRIDE = 1.500000
MAX_SPINDLE_OVERRIDE = 1.500000
MIN_SPINDLE_OVERRIDE = 0.500000
INTRO_GRAPHIC = linuxcnc.gif
INTRO_TIME = 5
PROGRAM_PREFIX = /home/emco/linuxcnc/nc_files
PYVCP = pyvcp-panel.xml
INCREMENTS = 5mm 1mm .5mm .1mm .05mm .01mm .005mm
LATHE = 1
POSITION_FEEDBACK = ACTUAL
DEFAULT_LINEAR_VELOCITY = 6.000000
MAX_LINEAR_VELOCITY = 25.000000
MIN_LINEAR_VELOCITY = 0.500000
DEFAULT_ANGULAR_VELOCITY = 12.000000
MAX_ANGULAR_VELOCITY = 180.000000
MIN_ANGULAR_VELOCITY = 1.666667
EDITOR = gedit
GEOMETRY = xyz
BACK_TOOL_LATHE = 1

[FILTER]
PROGRAM_EXTENSION = .png,.gif,.jpg Greyscale Depth Image
PROGRAM_EXTENSION = .py Python Script
png = image-to-gcode
gif = image-to-gcode
jpg = image-to-gcode
py = python

[TASK]
TASK = milltask
CYCLE_TIME = 0.010

[RS274NGC]
PARAMETER_FILE = linuxcnc.var
USER_M_PATH = /home/emco/linuxcnc/configs/EMCOTURN220/M-codes/


[EMCMOT]
EMCMOT = motmod
COMM_TIMEOUT = 1.0
COMM_WAIT = 0.010
SERVO_PERIOD = 1000000

[HOSTMOT2]
# **** This is for info only ****
# DRIVER0=hm2_eth
# BOARD0=7i76e

[HAL]
HALUI = halui
HALFILE = EMCOTURN220.hal
HALFILE = custom.hal
POSTGUI_HALFILE = postgui_call_list.hal
SHUTDOWN = shutdown.hal

[HALUI]

[TRAJ]
AXES = 3
COORDINATES = X Z
LINEAR_UNITS = mm
ANGULAR_UNITS = degree
CYCLE_TIME = 0.010
DEFAULT_VELOCITY = 11.67
MAX_VELOCITY = 116.67

[EMCIO]
EMCIO = io
CYCLE_TIME = 0.100
TOOL_TABLE = tool.tbl

#********************
# Axis X
#********************
[AXIS_0]
TYPE = LINEAR
HOME = 0.0
FERROR = 10.0
MIN_FERROR = 1.0
MAX_VELOCITY = 116.666666667
MAX_ACCELERATION = 750.0
# The values below should be 25% larger than MAX_VELOCITY and MAX_ACCELERATION
# If using BACKLASH compensation STEPGEN_MAXACCEL should be 100% larger.
STEPGEN_MAXVEL = 145.83
STEPGEN_MAXACCEL = 937.50
P = 1000.0
I = 0.0
D = 0.0
FF0 = 0.0
FF1 = 1.0
FF2 = 0.0
BIAS = 0.0
DEADBAND = 0.0
MAX_OUTPUT = 0.0
# these are in nanoseconds
DIRSETUP   = 1000
DIRHOLD    = 1000
STEPLEN    = 1000
STEPSPACE  = 1000
STEP_SCALE = -2000.0
BACKLASH = 0.015
MIN_LIMIT = -56.0
MAX_LIMIT = 0.0
HOME_OFFSET = 0.000000
HOME_SEARCH_VEL = -35.000000
HOME_LATCH_VEL = -1.500000
HOME_FINAL_VEL = 0.500000
HOME_USE_INDEX = NO
HOME_SEQUENCE = 1

#********************
# Axis Z
#********************
[AXIS_2]
TYPE = LINEAR
HOME = 0.0
FERROR = 10.0
MIN_FERROR = 1.0
MAX_VELOCITY = 116.666666667
MAX_ACCELERATION = 750.0
# The values below should be 25% larger than MAX_VELOCITY and MAX_ACCELERATION
# If using BACKLASH compensation STEPGEN_MAXACCEL should be 100% larger.
STEPGEN_MAXVEL = 145.83
STEPGEN_MAXACCEL = 937.50
P = 1000.0
I = 0.0
D = 0.0
FF0 = 0.0
FF1 = 1.0
FF2 = 0.0
BIAS = 0.0
DEADBAND = 0.0
MAX_OUTPUT = 0.0
# these are in nanoseconds
DIRSETUP   = 1000
DIRHOLD    = 1000
STEPLEN    = 1000
STEPSPACE  = 1000
STEP_SCALE = 2000.0
BACKLASH = 0.01
MIN_LIMIT = -175.0
MAX_LIMIT = 0.01
HOME_OFFSET = 0.000000
HOME_SEARCH_VEL = -35.000000
HOME_LATCH_VEL = -1.500000
HOME_FINAL_VEL = 0.500000
HOME_USE_INDEX = NO
HOME_SEQUENCE = 0

#********************
# Spindle 
#********************
[SPINDLE_9]
P = 10.50
I = 0.1
D = 0.15
FF0 = 1.07
FF1 = 0.0
FF2 = 0.0
BIAS = 0.0
DEADBAND = 0.0
MAX_OUTPUT = 6000
ENCODER_SCALE = 4096
OUTPUT_SCALE = 5700
OUTPUT_MIN_LIMIT = 0.0
OUTPUT_MAX_LIMIT = 6000