[    5.627340] EtherCAT: Master driver 1.6.0-rc1 unknown

[    5.627452] EtherCAT: 1 master waiting for devices.

[    5.635705] ec_generic: EtherCAT master generic Ethernet device module 1.6.0-rc1 unknown

[    5.635714] EtherCAT: Accepting 1C:1B:0D:12:9F:8F as main device for master 0.

[    5.635726] ec_generic: Binding socket to interface 2 (enp1s0).

[    5.666467] EtherCAT 0: Starting EtherCAT-IDLE thread.

[    5.666668] EtherCAT 0: Link state of ecm0 changed to UP.

[    5.674399] EtherCAT WARNING 0: 1 datagram TIMED OUT!

[    6.182096] IPv6: ADDRCONF(NETDEV_UP): enp1s0: link is not ready

[    6.183690] r8169 0000:01:00.0: firmware: failed to load rtl_nic/rtl8168g-2.fw (-2)

[    6.184341] r8169 0000:01:00.0: Direct firmware load for rtl_nic/rtl8168g-2.fw failed with error -2

[    6.184344] r8169 0000:01:00.0 enp1s0: unable to load firmware patch rtl_nic/rtl8168g-2.fw (-2)

[    6.184571] Generic PHY r8169-100:00: attached PHY driver [Generic PHY] (mii_bus:phy_addr=r8169-100:00, irq=IGNORE)

[    6.190351] EtherCAT 0: Link state of ecm0 changed to DOWN.

[    6.284799] IPv6: ADDRCONF(NETDEV_UP): enp1s0: link is not ready

[    6.317610] IPv6: ADDRCONF(NETDEV_UP): enx006f000126bb: link is not ready

[    6.319923] IPv6: ADDRCONF(NETDEV_UP): enx006f000126bb: link is not ready

[    6.668969] IPv6: ADDRCONF(NETDEV_CHANGE): enx006f000126bb: link becomes ready

[    6.677326] asix 1-8:1.0 enx006f000126bb: link up, 100Mbps, full-duplex, lpa 0xC5E1

[    6.977853] broken atomic modeset userspace detected, disabling atomic

[    7.917529] r8169 0000:01:00.0 enp1s0: Link is Up - 100Mbps/Full - flow control off

[    7.917548] IPv6: ADDRCONF(NETDEV_CHANGE): enp1s0: link becomes ready

[    7.922397] EtherCAT 0: Link state of ecm0 changed to UP.

[    7.930401] EtherCAT 0: 1 slave(s) responding on main device.

[    7.930406] EtherCAT 0: Slave states on main device: PREOP.

[    7.930502] EtherCAT 0: Scanning bus.

[    7.940800] EtherCAT 0: Bus scanning completed in 8 ms.

[    7.940803] EtherCAT 0: Using slave 0 as DC reference clock.

[    8.493519] fuse init (API version 7.27)

[   11.220067] rfkill: input handler disabled

[  260.551951] EtherCAT: Requesting master 0...

[  260.551953] EtherCAT: Successfully requested master 0.

[  260.552139] EtherCAT 0: Domain0: Logical address 0x00000000, 46 byte, expected working counter 3.

[  260.552141] EtherCAT 0:   Datagram domain0-0-main: Logical offset 0x00000000, 46 byte, type LRW at 000000006b7f61bb.

[  260.552148] EtherCAT 0: Master thread exited.

[  260.552149] EtherCAT 0: Starting EtherCAT-OP thread.

[  260.552170] EtherCAT WARNING 0: 61 datagrams TIMED OUT!

[  260.811521] EtherCAT ERROR 0-0: SDO download 0x1C12:00 (1 bytes) aborted.

[  260.811525] EtherCAT ERROR 0-0: SDO abort message 0x06040041: "The object cannot be mapped into the PDO".

[  260.811526] EtherCAT WARNING 0-0: Failed to set number of assigned PDOs of SM2.

[  260.811527] EtherCAT WARNING 0-0: Currently assigned PDOs: (none). PDOs to assign: 0x1600

[  260.811529] EtherCAT WARNING 0-0: PDO configuration failed.

[  260.820520] EtherCAT ERROR 0-0: Failed to set SAFEOP state, slave refused state change (PREOP + ERROR).

[  260.821519] EtherCAT ERROR 0-0: AL status message 0x001E: "Invalid input configuration".

[  260.823519] EtherCAT 0-0: Acknowledged state PREOP.

[  351.420464] EtherCAT 0: Master thread exited.

[  351.420470] EtherCAT 0: Starting EtherCAT-IDLE thread.

[  351.420500] EtherCAT 0: 0 slave(s) responding on main device.

[  351.420504] EtherCAT 0: Releasing master...

[  351.420505] EtherCAT 0: Released.

[  351.435841] EtherCAT 0: 1 slave(s) responding on main device.

[  351.435843] EtherCAT 0: Slave states on main device: PREOP.

[  351.436084] EtherCAT 0: Scanning bus.

[  351.444888] EtherCAT 0: Bus scanning completed in 8 ms.

[  351.444889] EtherCAT 0: Using slave 0 as DC reference clock.

[  351.807908] EtherCAT WARNING: Datagram 00000000106fcb72 (master-fsm) was SKIPPED 1 time.

[  377.082392] EtherCAT: Requesting master 0...

[  377.082394] EtherCAT: Successfully requested master 0.

[  377.082579] EtherCAT 0: Domain0: Logical address 0x00000000, 46 byte, expected working counter 3.

[  377.082581] EtherCAT 0:   Datagram domain0-0-main: Logical offset 0x00000000, 46 byte, type LRW at 0000000033dd0c22.

[  377.082589] EtherCAT 0: Master thread exited.

[  377.082590] EtherCAT 0: Starting EtherCAT-OP thread.

[  377.082656] EtherCAT WARNING 0: 1 datagram UNMATCHED!

[  377.273624] EtherCAT ERROR 0-0: SDO download 0x1C12:00 (1 bytes) aborted.

[  377.273628] EtherCAT ERROR 0-0: SDO abort message 0x06040041: "The object cannot be mapped into the PDO".

[  377.273629] EtherCAT WARNING 0-0: Failed to set number of assigned PDOs of SM2.

[  377.273630] EtherCAT WARNING 0-0: Currently assigned PDOs: (none). PDOs to assign: 0x1600

[  377.273632] EtherCAT WARNING 0-0: PDO configuration failed.

[  377.283643] EtherCAT ERROR 0-0: Failed to set SAFEOP state, slave refused state change (PREOP + ERROR).

[  377.284627] EtherCAT ERROR 0-0: AL status message 0x001E: "Invalid input configuration".

[  377.286626] EtherCAT 0-0: Acknowledged state PREOP.

[ 1431.883946] EtherCAT 0: Master debug level set to 1.

[ 1443.771686] EtherCAT DEBUG 0: ecrt_master_deactivate(master = 0x00000000e12cb347)

[ 1443.771687] EtherCAT DEBUG 0: Stopping master thread.

[ 1443.771691] EtherCAT DEBUG 0: Master OP thread exiting...

[ 1443.771697] EtherCAT 0: Master thread exited.

[ 1443.771701] EtherCAT 0: Starting EtherCAT-IDLE thread.

[ 1443.771730] EtherCAT DEBUG 0: Idle thread running with send interval = 4000 us, max data size=45000

[ 1443.771733] EtherCAT DEBUG 0: UNMATCHED datagram:

[ 1443.771734] EtherCAT DEBUG: 0C 9F 00 00 00 00 2E 80 00 00 04 00 00 00 00 00

[ 1443.771737] EtherCAT DEBUG: 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00 00

[ 1443.771739] EtherCAT DEBUG: 00

[ 1443.771740] EtherCAT 0: Releasing master...

[ 1443.771740] 00 00 00 00 00

[ 1443.771742] EtherCAT DEBUG 0: OPERATION -> IDLE.

[ 1443.771742] 00 00 00

[ 1443.771743] EtherCAT 0: Released.

[ 1443.771743] 00 00 00 00 00 00 00

[ 1443.771745] EtherCAT DEBUG: 00 00 00 00 00 00 00 00 00 00

[ 1443.771748] EtherCAT 0: 0 slave(s) responding on main device.

[ 1443.771859] EtherCAT DEBUG 0: Datagram 00000000106fcb72 already queued (skipping).

[ 1443.776027] EtherCAT 0: 1 slave(s) responding on main device.

[ 1443.776029] EtherCAT 0: Slave states on main device: PREOP.

[ 1443.776062] EtherCAT DEBUG 0: Sending broadcast-write to measure transmission delays on main link.

[ 1443.776084] EtherCAT DEBUG 0: 1 slaves responded to delay measuring on main link.

[ 1443.776084] EtherCAT 0: Scanning bus.

[ 1443.776085] EtherCAT DEBUG 0: Scanning slave 0 on main link.

[ 1443.776169] EtherCAT DEBUG 0-0: Slave has the System Time register.

[ 1443.776211] EtherCAT DEBUG 0-0: Port 0 link status changed to up.

[ 1443.776212] EtherCAT DEBUG 0-0: Port 0 loop status changed to open.

[ 1443.776213] EtherCAT DEBUG 0-0: Port 0 signal status changed to yes.

[ 1443.776213] EtherCAT DEBUG 0-0: Assigning SII access to EtherCAT.

[ 1443.776235] EtherCAT DEBUG 0-0: Determining SII size.

[ 1443.776295] EtherCAT DEBUG 0-0: Found category type 40 with size 2. Proceeding to offset 68.

[ 1443.776377] EtherCAT DEBUG 0-0: Found category type 30 with size 16. Proceeding to offset 86.

[ 1443.776418] EtherCAT DEBUG 0-0: Found category type 41 with size 16. Proceeding to offset 104.

[ 1443.779395] EtherCAT DEBUG 0-0: Slave announces to support CoE, FoE.

[ 1443.779396] EtherCAT DEBUG 0-0: Slave announces to support unknown mailbox protocols 0x0002.

[ 1443.779397] EtherCAT DEBUG 0-0: Reading mailbox sync manager configuration.

[ 1443.779419] EtherCAT DEBUG 0-0: Mailbox configuration:

[ 1443.779420] EtherCAT DEBUG 0-0:  RX offset=0x1000 size=128

[ 1443.779420] EtherCAT DEBUG 0-0:  TX offset=0x1080 size=128

[ 1443.779421] EtherCAT DEBUG 0-0: Scanning PDO assignment and mapping.

[ 1443.779422] EtherCAT DEBUG 0-0: Reading PDO assignment of SM2.

[ 1443.779424] EtherCAT DEBUG 0-0: Uploading SDO 0x1C12:00.

[ 1443.779424] EtherCAT DEBUG 0-0: Upload request:

[ 1443.779425] EtherCAT DEBUG: 00 20 40 12 1C 00 00 00 00 00

[ 1443.780350] EtherCAT DEBUG 0-0: Upload response:

[ 1443.780350] EtherCAT DEBUG: 00 30 4F 12 1C 00 00 00 00 00

[ 1443.780353] EtherCAT DEBUG 0-0: Uploaded data:

[ 1443.780353] EtherCAT DEBUG: 00

[ 1443.780354] EtherCAT DEBUG 0-0: 0 PDOs assigned.

[ 1443.780355] EtherCAT DEBUG 0-0: Reading PDO assignment of SM3.

[ 1443.780356] EtherCAT DEBUG 0-0: Uploading SDO 0x1C13:00.

[ 1443.780356] EtherCAT DEBUG 0-0: Upload request:

[ 1443.780357] EtherCAT DEBUG: 00 20 40 13 1C 00 00 00 00 00

[ 1443.781305] EtherCAT DEBUG 0-0: Upload response:

[ 1443.781305] EtherCAT DEBUG: 00 30 4F 13 1C 00 01 00 00 00

[ 1443.781308] EtherCAT DEBUG 0-0: Uploaded data:

[ 1443.781308] EtherCAT DEBUG: 01

[ 1443.781309] EtherCAT DEBUG 0-0: 1 PDOs assigned.

[ 1443.781310] EtherCAT DEBUG 0-0: Uploading SDO 0x1C13:01.

[ 1443.781310] EtherCAT DEBUG 0-0: Upload request:

[ 1443.781311] EtherCAT DEBUG: 00 20 40 13 1C 01 00 00 00 00

[ 1443.782198] EtherCAT DEBUG 0-0: Upload response:

[ 1443.782198] EtherCAT DEBUG: 00 30 4B 13 1C 01 01 1A 00 00

[ 1443.782200] EtherCAT DEBUG 0-0: Uploaded data:

[ 1443.782200] EtherCAT DEBUG: 01 1A

[ 1443.782202] EtherCAT DEBUG 0-0: PDO 0x1A01.

[ 1443.782203] EtherCAT DEBUG 0-0: Uploading SDO 0x1A01:00.

[ 1443.782208] EtherCAT DEBUG 0-0: Upload request:

[ 1443.782208] EtherCAT DEBUG: 00 20 40 01 1A 00 00 00 00 00

[ 1443.782971] EtherCAT DEBUG 0-0: Upload response:

[ 1443.782971] EtherCAT DEBUG: 00 30 4F 01 1A 00 02 00 00 00

[ 1443.782973] EtherCAT DEBUG 0-0: Uploaded data:

[ 1443.782974] EtherCAT DEBUG: 02

[ 1443.782975] EtherCAT DEBUG 0-0: 2 PDO entries mapped.

[ 1443.782976] EtherCAT DEBUG 0-0: Uploading SDO 0x1A01:01.

[ 1443.782976] EtherCAT DEBUG 0-0: Upload request:

[ 1443.782976] EtherCAT DEBUG: 00 20 40 01 1A 01 00 00 00 00

[ 1443.783940] EtherCAT DEBUG 0-0: Upload response:

[ 1443.783941] EtherCAT DEBUG: 00 30 43 01 1A 01 10 00 41 60

[ 1443.783943] EtherCAT DEBUG 0-0: Uploaded data:

[ 1443.783943] EtherCAT DEBUG: 10 00 41 60

[ 1443.783945] EtherCAT DEBUG 0-0: PDO entry 0x6041:00, 16 bit, "???".

[ 1443.783946] EtherCAT DEBUG 0-0: Uploading SDO 0x1A01:02.

[ 1443.783946] EtherCAT DEBUG 0-0: Upload request:

[ 1443.783947] EtherCAT DEBUG: 00 20 40 01 1A 02 00 00 00 00

[ 1443.784855] EtherCAT DEBUG 0-0: Upload response:

[ 1443.784855] EtherCAT DEBUG: 00 30 43 01 1A 02 20 00 64 60

[ 1443.784863] EtherCAT DEBUG 0-0: Uploaded data:

[ 1443.784864] EtherCAT DEBUG: 20 00 64 60

[ 1443.784866] EtherCAT DEBUG 0-0: PDO entry 0x6064:00, 32 bit, "???".

[ 1443.784867] EtherCAT DEBUG 0-0: Reading of PDO configuration finished.

[ 1443.784868] EtherCAT 0: Bus scanning completed in 8 ms.

[ 1443.784870] EtherCAT 0: Using slave 0 as DC reference clock.

[ 1443.784871] EtherCAT DEBUG 0-0: ec_slave_calc_transmission_delays_rec(delay = 0 ns)

[ 1443.784872] EtherCAT DEBUG 0: No app_time received up to now.

[ 1443.800010] EtherCAT DEBUG 0-0: Changing state from PREOP to PREOP (forced).

[ 1443.800011] EtherCAT DEBUG 0-0: Configuring...

[ 1443.800353] EtherCAT DEBUG 0-0: Now in INIT.

[ 1443.800354] EtherCAT DEBUG 0-0: Clearing FMMU configurations...

[ 1443.800354] EtherCAT DEBUG 0-0: Clearing mailbox check flag...

[ 1443.800377] EtherCAT DEBUG 0-0: Clearing sync manager configurations...

[ 1443.800398] EtherCAT DEBUG 0-0: Clearing DC assignment...

[ 1443.800419] EtherCAT DEBUG 0-0: Configuring mailbox sync managers...

[ 1443.800420] EtherCAT DEBUG 0-0: SM0: Addr 0x1000, Size 128, Ctrl 0x36, En 1

[ 1443.800421] EtherCAT DEBUG 0-0: SM1: Addr 0x1080, Size 128, Ctrl 0x32, En 1

[ 1443.800442] EtherCAT DEBUG 0-0: Assigning SII access to PDI.

[ 1443.800703] EtherCAT DEBUG 0-0: Now in PREOP.

[ 1443.800704] EtherCAT DEBUG 0-0: Assigning SII access back to EtherCAT.

[ 1443.800724] EtherCAT DEBUG 0-0: Finished configuration.

[ 1443.871974] EtherCAT WARNING: Datagram 00000000106fcb72 (master-fsm) was SKIPPED 1 time.

[ 1446.807914] EtherCAT DEBUG 0-0: Fetching SDO dictionary.

[ 1446.823500] EtherCAT DEBUG 0-0: SDO list fragments left: 5

[ 1446.823766] EtherCAT DEBUG 0-0: SDO list fragments left: 4

[ 1446.824023] EtherCAT DEBUG 0-0: SDO list fragments left: 3

[ 1446.824423] EtherCAT DEBUG 0-0: SDO list fragments left: 2

[ 1446.825419] EtherCAT DEBUG 0-0: SDO list fragments left: 1

[ 1447.723013] EtherCAT DEBUG 0-0: Fetched 316 SDOs and 1002 entries.

[ 1447.723014] EtherCAT DEBUG 0-0: Ready for requests.

[ 1448.047712] EtherCAT: Requesting master 0...

[ 1448.047713] EtherCAT DEBUG 0: IDLE -> OPERATION.

[ 1448.047714] EtherCAT: Successfully requested master 0.

[ 1448.047717] EtherCAT DEBUG 0: ecrt_master_create_domain(master = 0x00000000e12cb347)

[ 1448.047718] EtherCAT DEBUG 0: Created domain 0.

[ 1448.047719] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047720] EtherCAT DEBUG 0: Creating slave configuration for 0:0, 0x00000539/0x02200301.

[ 1448.047721] EtherCAT DEBUG 0 0:0: Attached slave 0.

[ 1448.047843] EtherCAT DEBUG 0 0:0: ecrt_slave_config_dc(sc = 0x000000005908b22b, assign_activate = 0x0300, sync0_cycle = 1000000, sync0_shift = 0, sync1_cycle = 0, sync1_shift = 0

[ 1448.047845] EtherCAT DEBUG 0 0:0: ecrt_slave_config_sync_manager(sc = 0x000000005908b22b, sync_index = 2, dir = 1, watchdog_mode = 0)

[ 1448.047846] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_assign_clear(sc = 0x000000005908b22b, sync_index = 2)

[ 1448.047848] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_assign_add(sc = 0x000000005908b22b, sync_index = 2, pdo_index = 0x1600)

[ 1448.047849] EtherCAT DEBUG 0 0:0: Loading default mapping for PDO 0x1600.

[ 1448.047849] EtherCAT DEBUG 0 0:0: No default mapping found.

[ 1448.047853] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_clear(sc = 0x000000005908b22b, pdo_index = 0x1600)

[ 1448.047856] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x6040, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047858] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x6060, entry_subindex = 0x00, entry_bit_length = 8)

[ 1448.047860] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x607A, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047861] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x60FF, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047862] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x6071, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047864] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x6072, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047865] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x60B8, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047868] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1600, entry_index = 0x204A, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047871] EtherCAT DEBUG 0 0:0: ecrt_slave_config_sync_manager(sc = 0x000000005908b22b, sync_index = 3, dir = 2, watchdog_mode = 0)

[ 1448.047872] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_assign_clear(sc = 0x000000005908b22b, sync_index = 3)

[ 1448.047873] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_assign_add(sc = 0x000000005908b22b, sync_index = 3, pdo_index = 0x1A00)

[ 1448.047874] EtherCAT DEBUG 0 0:0: Loading default mapping for PDO 0x1A00.

[ 1448.047875] EtherCAT DEBUG 0 0:0: No default mapping found.

[ 1448.047876] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_clear(sc = 0x000000005908b22b, pdo_index = 0x1A00)

[ 1448.047879] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x6041, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047881] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x6061, entry_subindex = 0x00, entry_bit_length = 8)

[ 1448.047883] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x6064, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047884] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x606C, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047885] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x6077, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047887] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x60F4, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047888] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x60B9, entry_subindex = 0x00, entry_bit_length = 16)

[ 1448.047890] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x60BA, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047891] EtherCAT DEBUG 0 0:0: ecrt_slave_config_pdo_mapping_add(sc = 0x000000005908b22b, pdo_index = 0x1A00, entry_index = 0x60FD, entry_subindex = 0x00, entry_bit_length = 32)

[ 1448.047915] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047917] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6040, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047918] EtherCAT DEBUG 0: Domain 0: Added 19 bytes at 0.

[ 1448.047920] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047921] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6060, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047923] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047924] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x607A, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047925] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047927] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FF, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047928] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047930] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6071, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047931] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047932] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6072, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047933] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047935] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60B8, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047936] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047938] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x204A, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047939] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047941] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x204A, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047942] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047943] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6041, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047944] EtherCAT DEBUG 0: Domain 0: Added 27 bytes at 19.

[ 1448.047945] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047947] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6061, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047948] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047950] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6064, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047951] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047953] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x606C, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047954] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047955] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x6077, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047957] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047959] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60F4, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047960] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047962] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60B9, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047963] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047964] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60BA, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047965] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047967] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047968] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047970] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047971] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047972] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047973] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047975] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047976] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047978] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047979] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047980] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047981] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047983] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047984] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047985] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.047987] EtherCAT DEBUG 0: ecrt_master_slave_config(master = 0x00000000e12cb347, alias = 0, position = 0, vendor_id = 0x00000539, product_code = 0x02200301)

[ 1448.047988] EtherCAT DEBUG 0 0:0: ecrt_slave_config_reg_pdo_entry(sc = 0x000000005908b22b, index = 0x60FD, subindex = 0x00, domain = 0x000000003e89b103, bit_position = 0x000000000cc9196e)

[ 1448.048008] EtherCAT DEBUG 0: ecrt_domain_external_memory(domain = 0x000000003e89b103, mem = 0x000000004e52fd04)

[ 1448.048009] EtherCAT DEBUG 0: ecrt_master_callbacks(master = 0x00000000e12cb347, send_cb = 0x00000000279f4820, receive_cb = 0x00000000d292ac9c, cb_data = 0x00000000e12cb347)

[ 1448.048009] EtherCAT DEBUG 0: ecrt_master_activate(master = 0x00000000e12cb347)

[ 1448.048011] EtherCAT DEBUG 0: Adding datagram pair with expected WC 3.

[ 1448.048011] EtherCAT 0: Domain0: Logical address 0x00000000, 46 byte, expected working counter 3.

[ 1448.048012] EtherCAT 0:   Datagram domain0-0-main: Logical offset 0x00000000, 46 byte, type LRW at 000000008318b2df.

[ 1448.048014] EtherCAT DEBUG 0: Stopping master thread.

[ 1448.048017] EtherCAT DEBUG 0: Master IDLE thread exiting...

[ 1448.048022] EtherCAT 0: Master thread exited.

[ 1448.048023] EtherCAT DEBUG 0: FSM datagram is 00000000106fcb72.

[ 1448.048024] EtherCAT 0: Starting EtherCAT-OP thread.

[ 1448.048046] EtherCAT DEBUG 0: Operation thread running with fsm interval = 4000 us, max data size=45000

[ 1448.048047] EtherCAT DEBUG 0: mmap()

[ 1448.048048] EtherCAT WARNING 0: 1 datagram UNMATCHED!

[ 1448.048050] EtherCAT DEBUG 0: Vma fault, offset = 0, page = 000000008ffca083

[ 1448.119817] EtherCAT DEBUG 0: Configuration changed.

[ 1448.119819] EtherCAT DEBUG 0-0: Checking system time offset.

[ 1448.131817] EtherCAT DEBUG 0-0: DC 32 bit system time offset calculation: system_time=148470481, app_time=728488382683516370, diff=4865

[ 1448.131819] EtherCAT DEBUG 0-0: Setting time offset to 1257391909 (was 1257387044)

[ 1448.151825] EtherCAT DEBUG 0: Requesting OP...

[ 1448.171821] EtherCAT DEBUG 0-0: Changing state from PREOP to OP.

[ 1448.171823] EtherCAT DEBUG 0-0: Configuring...

[ 1448.175085] EtherCAT DEBUG 0-0: Now in INIT.

[ 1448.175086] EtherCAT DEBUG 0-0: Clearing FMMU configurations...

[ 1448.175086] EtherCAT DEBUG 0-0: Clearing mailbox check flag...

[ 1448.177076] EtherCAT DEBUG 0-0: Clearing sync manager configurations...

[ 1448.179073] EtherCAT DEBUG 0-0: Clearing DC assignment...

[ 1448.181078] EtherCAT DEBUG 0-0: Configuring mailbox sync managers...

[ 1448.181080] EtherCAT DEBUG 0-0: SM0: Addr 0x1000, Size 128, Ctrl 0x36, En 1

[ 1448.181081] EtherCAT DEBUG 0-0: SM1: Addr 0x1080, Size 128, Ctrl 0x32, En 1

[ 1448.183079] EtherCAT DEBUG 0-0: Assigning SII access to PDI.

[ 1448.189076] EtherCAT DEBUG 0-0: Now in PREOP.

[ 1448.189078] EtherCAT DEBUG 0-0: Assigning SII access back to EtherCAT.

[ 1448.191077] EtherCAT DEBUG 0-0: Reading mapping of PDO 0x1600.

[ 1448.191078] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:00.

[ 1448.191079] EtherCAT DEBUG 0-0: Upload request:

[ 1448.191079] EtherCAT DEBUG: 00 20 40 00 16 00 00 00 00 00

[ 1448.197074] EtherCAT DEBUG 0-0: Upload response:

[ 1448.197075] EtherCAT DEBUG: 00 30 4F 00 16 00 08 00 00 00

[ 1448.197077] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.197078] EtherCAT DEBUG: 08

[ 1448.197079] EtherCAT DEBUG 0-0: 8 PDO entries mapped.

[ 1448.197080] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:01.

[ 1448.197080] EtherCAT DEBUG 0-0: Upload request:

[ 1448.197081] EtherCAT DEBUG: 00 20 40 00 16 01 00 00 00 00

[ 1448.203075] EtherCAT DEBUG 0-0: Upload response:

[ 1448.203076] EtherCAT DEBUG: 00 30 43 00 16 01 10 00 40 60

[ 1448.203078] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.203079] EtherCAT DEBUG: 10 00 40 60

[ 1448.203081] EtherCAT DEBUG 0-0: PDO entry 0x6040:00, 16 bit, "???".

[ 1448.203081] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:02.

[ 1448.203082] EtherCAT DEBUG 0-0: Upload request:

[ 1448.203082] EtherCAT DEBUG: 00 20 40 00 16 02 00 00 00 00

[ 1448.209074] EtherCAT DEBUG 0-0: Upload response:

[ 1448.209075] EtherCAT DEBUG: 00 30 43 00 16 02 08 00 60 60

[ 1448.209077] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.209077] EtherCAT DEBUG: 08 00 60 60

[ 1448.209080] EtherCAT DEBUG 0-0: PDO entry 0x6060:00, 8 bit, "???".

[ 1448.209081] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:03.

[ 1448.209081] EtherCAT DEBUG 0-0: Upload request:

[ 1448.209082] EtherCAT DEBUG: 00 20 40 00 16 03 00 00 00 00

[ 1448.215083] EtherCAT DEBUG 0-0: Upload response:

[ 1448.215084] EtherCAT DEBUG: 00 30 43 00 16 03 20 00 7A 60

[ 1448.215086] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.215086] EtherCAT DEBUG: 20 00 7A 60

[ 1448.215088] EtherCAT DEBUG 0-0: PDO entry 0x607A:00, 32 bit, "???".

[ 1448.215089] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:04.

[ 1448.215089] EtherCAT DEBUG 0-0: Upload request:

[ 1448.215089] EtherCAT DEBUG: 00 20 40 00 16 04 00 00 00 00

[ 1448.221077] EtherCAT DEBUG 0-0: Upload response:

[ 1448.221078] EtherCAT DEBUG: 00 30 43 00 16 04 20 00 FF 60

[ 1448.221081] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.221081] EtherCAT DEBUG: 20 00 FF 60

[ 1448.221084] EtherCAT DEBUG 0-0: PDO entry 0x60FF:00, 32 bit, "???".

[ 1448.221085] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:05.

[ 1448.221086] EtherCAT DEBUG 0-0: Upload request:

[ 1448.221086] EtherCAT DEBUG: 00 20 40 00 16 05 00 00 00 00

[ 1448.227076] EtherCAT DEBUG 0-0: Upload response:

[ 1448.227076] EtherCAT DEBUG: 00 30 43 00 16 05 10 00 71 60

[ 1448.227079] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.227079] EtherCAT DEBUG: 10 00 71 60

[ 1448.227081] EtherCAT DEBUG 0-0: PDO entry 0x6071:00, 16 bit, "???".

[ 1448.227082] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:06.

[ 1448.227082] EtherCAT DEBUG 0-0: Upload request:

[ 1448.227083] EtherCAT DEBUG: 00 20 40 00 16 06 00 00 00 00

[ 1448.233073] EtherCAT DEBUG 0-0: Upload response:

[ 1448.233074] EtherCAT DEBUG: 00 30 43 00 16 06 10 00 72 60

[ 1448.233076] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.233077] EtherCAT DEBUG: 10 00 72 60

[ 1448.233078] EtherCAT DEBUG 0-0: PDO entry 0x6072:00, 16 bit, "???".

[ 1448.233079] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:07.

[ 1448.233080] EtherCAT DEBUG 0-0: Upload request:

[ 1448.233080] EtherCAT DEBUG: 00 20 40 00 16 07 00 00 00 00

[ 1448.239082] EtherCAT DEBUG 0-0: Upload response:

[ 1448.239083] EtherCAT DEBUG: 00 30 43 00 16 07 10 00 B8 60

[ 1448.239085] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.239086] EtherCAT DEBUG: 10 00 B8 60

[ 1448.239087] EtherCAT DEBUG 0-0: PDO entry 0x60B8:00, 16 bit, "???".

[ 1448.239088] EtherCAT DEBUG 0-0: Uploading SDO 0x1600:08.

[ 1448.239088] EtherCAT DEBUG 0-0: Upload request:

[ 1448.239089] EtherCAT DEBUG: 00 20 40 00 16 08 00 00 00 00

[ 1448.245075] EtherCAT DEBUG 0-0: Upload response:

[ 1448.245076] EtherCAT DEBUG: 00 30 43 00 16 08 10 00 4A 20

[ 1448.245079] EtherCAT DEBUG 0-0: Uploaded data:

[ 1448.245079] EtherCAT DEBUG: 10 00 4A 20

[ 1448.245081] EtherCAT DEBUG 0-0: PDO entry 0x204A:00, 16 bit, "???".

[ 1448.245082] EtherCAT DEBUG 0-0: Changing mapping of PDO 0x1600.

[ 1448.245082] EtherCAT DEBUG 0-0: Currently mapped PDO entries: 0x6040:00/16 0x6060:00/8 0x607A:00/32 0x60FF:00/32 0x6071:00/16 0x6072:00/16 0x60B8:00/16 0x204A:00/16. Entries to map: 0x6040:00/16 0x6060:00/8 0x607A:00/32 0x60FF:00/32 0x6071:00/16 0x6072:00/16 0x60B8:00/16 0x204A:00/16

[ 1448.245089] EtherCAT DEBUG 0-0: Setting entry count to zero.

[ 1448.245090] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:00.

[ 1448.245090] EtherCAT DEBUG: 00

[ 1448.245092] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.245092] EtherCAT DEBUG: 00 20 2F 00 16 00 00 00 00 00

[ 1448.251079] EtherCAT DEBUG 0-0: Download response:

[ 1448.251081] EtherCAT DEBUG: 00 30 62 00 16 00 00 00 00 00

[ 1448.251084] EtherCAT DEBUG 0-0: Mapping PDO entry 0x6040:00 (16 bit) at position 1.

[ 1448.251085] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:01.

[ 1448.251085] EtherCAT DEBUG: 10 00 40 60

[ 1448.251087] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.251087] EtherCAT DEBUG: 00 20 23 00 16 01 10 00 40 60

[ 1448.257081] EtherCAT DEBUG 0-0: Download response:

[ 1448.257082] EtherCAT DEBUG: 00 30 62 00 16 01 10 00 40 60

[ 1448.257085] EtherCAT DEBUG 0-0: Mapping PDO entry 0x6060:00 (8 bit) at position 2.

[ 1448.257086] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:02.

[ 1448.257087] EtherCAT DEBUG: 08 00 60 60

[ 1448.257088] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.257089] EtherCAT DEBUG: 00 20 23 00 16 02 08 00 60 60

[ 1448.263078] EtherCAT DEBUG 0-0: Download response:

[ 1448.263079] EtherCAT DEBUG: 00 30 62 00 16 02 08 00 60 60

[ 1448.263082] EtherCAT DEBUG 0-0: Mapping PDO entry 0x607A:00 (32 bit) at position 3.

[ 1448.263083] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:03.

[ 1448.263083] EtherCAT DEBUG: 20 00 7A 60

[ 1448.263085] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.263085] EtherCAT DEBUG: 00 20 23 00 16 03 20 00 7A 60

[ 1448.269080] EtherCAT DEBUG 0-0: Download response:

[ 1448.269081] EtherCAT DEBUG: 00 30 62 00 16 03 20 00 7A 60

[ 1448.269084] EtherCAT DEBUG 0-0: Mapping PDO entry 0x60FF:00 (32 bit) at position 4.

[ 1448.269086] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:04.

[ 1448.269086] EtherCAT DEBUG: 20 00 FF 60

[ 1448.269088] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.269088] EtherCAT DEBUG: 00 20 23 00 16 04 20 00 FF 60

[ 1448.275101] EtherCAT DEBUG 0-0: Download response:

[ 1448.275103] EtherCAT DEBUG: 00 30 62 00 16 04 20 00 FF 60

[ 1448.275107] EtherCAT DEBUG 0-0: Mapping PDO entry 0x6071:00 (16 bit) at position 5.

[ 1448.275108] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:05.

[ 1448.275109] EtherCAT DEBUG: 10 00 71 60

[ 1448.275110] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.275111] EtherCAT DEBUG: 00 20 23 00 16 05 10 00 71 60

[ 1448.281079] EtherCAT DEBUG 0-0: Download response:

[ 1448.281080] EtherCAT DEBUG: 00 30 62 00 16 05 10 00 71 60

[ 1448.281082] EtherCAT DEBUG 0-0: Mapping PDO entry 0x6072:00 (16 bit) at position 6.

[ 1448.281083] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:06.

[ 1448.281084] EtherCAT DEBUG: 10 00 72 60

[ 1448.281085] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.281086] EtherCAT DEBUG: 00 20 23 00 16 06 10 00 72 60

[ 1448.287099] EtherCAT DEBUG 0-0: Download response:

[ 1448.287100] EtherCAT DEBUG: 00 30 62 00 16 06 10 00 72 60

[ 1448.287103] EtherCAT DEBUG 0-0: Mapping PDO entry 0x60B8:00 (16 bit) at position 7.

[ 1448.287105] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:07.

[ 1448.287105] EtherCAT DEBUG: 10 00 B8 60

[ 1448.287107] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.287107] EtherCAT DEBUG: 00 20 23 00 16 07 10 00 B8 60

[ 1448.293073] EtherCAT DEBUG 0-0: Download response:

[ 1448.293074] EtherCAT DEBUG: 00 30 62 00 16 07 10 00 B8 60

[ 1448.293077] EtherCAT DEBUG 0-0: Mapping PDO entry 0x204A:00 (16 bit) at position 8.

[ 1448.293078] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:08.

[ 1448.293078] EtherCAT DEBUG: 10 00 4A 20

[ 1448.293080] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.293080] EtherCAT DEBUG: 00 20 23 00 16 08 10 00 4A 20

[ 1448.299070] EtherCAT DEBUG 0-0: Download response:

[ 1448.299071] EtherCAT DEBUG: 00 30 62 00 16 08 10 00 4A 20

[ 1448.299073] EtherCAT DEBUG 0-0: Setting number of PDO entries to 8.

[ 1448.299073] EtherCAT DEBUG 0-0: Downloading SDO 0x1600:00.

[ 1448.299074] EtherCAT DEBUG: 08

[ 1448.299075] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.299075] EtherCAT DEBUG: 00 20 2F 00 16 00 08 00 00 00

[ 1448.305076] EtherCAT DEBUG 0-0: Download response:

[ 1448.305077] EtherCAT DEBUG: 00 30 62 00 16 00 08 00 00 00

[ 1448.305079] EtherCAT DEBUG 0-0: Successfully configured mapping for PDO 0x1600.

[ 1448.305080] EtherCAT DEBUG 0-0: Setting PDO assignment of SM2:

[ 1448.305081] EtherCAT DEBUG 0-0: Currently assigned PDOs: (none). PDOs to assign: 0x1600

[ 1448.305083] EtherCAT DEBUG 0-0: Setting number of assigned PDOs to zero.

[ 1448.305083] EtherCAT DEBUG 0-0: Downloading SDO 0x1C12:00.

[ 1448.305084] EtherCAT DEBUG: 00

[ 1448.305085] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.305085] EtherCAT DEBUG: 00 20 2F 12 1C 00 00 00 00 00

[ 1448.311071] EtherCAT DEBUG 0-0: Download response:

[ 1448.311072] EtherCAT DEBUG: 00 30 62 12 1C 00 00 00 00 00

[ 1448.311075] EtherCAT DEBUG 0-0: Assigning PDO 0x1600 at position 1.

[ 1448.311076] EtherCAT DEBUG 0-0: Downloading SDO 0x1C12:01.

[ 1448.311076] EtherCAT DEBUG: 00 16

[ 1448.311077] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.311078] EtherCAT DEBUG: 00 20 2B 12 1C 01 00 16 00 00

[ 1448.317071] EtherCAT DEBUG 0-0: Download response:

[ 1448.317071] EtherCAT DEBUG: 00 30 62 12 1C 01 00 16 00 00

[ 1448.317073] EtherCAT DEBUG 0-0: Setting number of assigned PDOs to 1.

[ 1448.317074] EtherCAT DEBUG 0-0: Downloading SDO 0x1C12:00.

[ 1448.317074] EtherCAT DEBUG: 01

[ 1448.317075] EtherCAT DEBUG 0-0: Expedited download request:

[ 1448.317076] EtherCAT DEBUG: 00 20 2F 12 1C 00 01 00 00 00

[ 1448.323087] EtherCAT DEBUG 0-0: Download response:

[ 1448.323088] EtherCAT DEBUG: 00 20 80 12 1C 00 41 00 04 06

[ 1448.323091] EtherCAT ERROR 0-0: SDO download 0x1C12:00 (1 bytes) aborted.

[ 1448.323094] EtherCAT ERROR 0-0: SDO abort message 0x06040041: "The object cannot be mapped into the PDO".

[ 1448.323096] EtherCAT WARNING 0-0: Failed to set number of assigned PDOs of SM2.

[ 1448.323096] EtherCAT WARNING 0-0: Currently assigned PDOs: (none). PDOs to assign: 0x1600

[ 1448.323098] EtherCAT WARNING 0-0: PDO configuration failed.

[ 1448.323101] EtherCAT DEBUG 0-0: SM2: Addr 0x1100, Size  19, Ctrl 0x74, En 1

[ 1448.323103] EtherCAT DEBUG 0-0: SM3: Addr 0x1400, Size  27, Ctrl 0x30, En 1

[ 1448.325087] EtherCAT DEBUG 0 0:0: FMMU: LogOff 0x00000000, Size  19, PhysAddr 0x1100, SM2, Dir out

[ 1448.325089] EtherCAT DEBUG 0 0:0: FMMU: LogOff 0x00000013, Size  27, PhysAddr 0x1400, SM3, Dir in

[ 1448.327071] EtherCAT DEBUG 0-0: Setting DC cycle times to 1000000 / 0.

[ 1448.329079] EtherCAT DEBUG 0-0: Checking for synchrony.

[ 1448.331072] EtherCAT DEBUG 0-0: -3862 ns difference after 0 ms.

[ 1448.331073] EtherCAT DEBUG 0-0:    ref_time=728488382611427000

[ 1448.331073] EtherCAT DEBUG 0-0:    app_time=728488382894507928

[ 1448.331074] EtherCAT DEBUG 0-0:  start_time=728488382994507928

[ 1448.331074] EtherCAT DEBUG 0-0:       cycle=1000000

[ 1448.331075] EtherCAT DEBUG 0-0:  shift_time=0

[ 1448.331075] EtherCAT DEBUG 0-0:   remainder=80928

[ 1448.331076] EtherCAT DEBUG 0-0:        start=728488382995427000

[ 1448.331077] EtherCAT DEBUG 0-0: Setting DC cyclic operation start time to 728488382995427000.

[ 1448.333070] EtherCAT DEBUG 0-0: Setting DC AssignActivate to 0x0300.

[ 1448.339071] EtherCAT ERROR 0-0: Failed to set SAFEOP state, slave refused state change (PREOP + ERROR).

[ 1448.341075] EtherCAT ERROR 0-0: AL status message 0x001E: "Invalid input configuration".

[ 1448.345071] EtherCAT 0-0: Acknowledged state PREOP.